## Slide 1: IoT and U can 2
Part 2, Controlling the World
Chad Boschert, Gravitate Solutions

## Slide 2: What is the Internet of Things?
  Devices + Network Connectivity + Exchange Data
  Integrating physical world and computer world
  Improved efficiency, accuracy, and economic benefit
https://en.wikipedia.org/wiki/Internet_of_Things
Notes: The Internet of Things (IoT) is the network of physical objects—devices, vehicles, buildings and other items—embedded withelectronics, software, sensors, and network connectivity that enables these objects to collect and exchange data.[1] The IoT allows objects to be sensed and controlled remotely across existing network infrastructure,[2] creating opportunities for more direct integration of the physical world into computer-based systems, and resulting in improved efficiency, accuracy and economic benefit;[3][4][5][6][7][8] when IoT is augmented with sensors and actuators, the technology becomes an instance of the more general class of cyber-physical systems, which also encompasses technologies such as smart grids, smart homes,intelligent transportation and smart cities. Each thing is uniquely identifiable through its embedded computing system but is able to interoperate within the existing Internet infrastructure. Experts estimate that the IoT will consist of almost 50 billion objects by 2020.[9]

## Slide 3: Raspberry Pi
Multiple versions, $5 to ~$40
Raspberry Pi 2
  900MHz quad-cord CPU
  1 GB RAM
  Micro SD card slot
  40 GPIO Pins
  4 USB Ports
  Full HDMI port
  Camera & Display interfaces
  Combined 3.5mm audio jack & composite video
https://www.raspberrypi.org/products/raspberry-pi-2-model-b/

## Slide 4: Fermonitor
DIY Wine Fermentation Temperature Control System

## Slide 5
Demo Time

## Slide 6: Design Principals
Be lean
  Keep it simple
  Create value
  If it already exists, use it
  Make it work, then improve later if needed
YAGNI
Learn

## Slide 7: Intro to GPIO
General-Purpose Input/Output
Simply, switches
  Inputs – controlled externally
  Output – controlled by the Pi
Ground
  Zero volts, completes circuits
3.3v
  Provides 3.3 volt power supply
5v
  Provides 5 volt power supply
GPIO #
  Configured as input/output
https://www.raspberrypi.org/learning/physical-computing-with-python/
https://sourceforge.net/p/raspberry-gpio-python/wiki/BasicUsage/

## Slide 8: Simple Circuit
Always On
https://www.raspberrypi.org/learning/physical-computing-with-python/worksheet/

## Slide 9: GPIO Circuit
Programmatically interactive
  switch off/on
GPIO.output(17, GPIO.LOW)
GPIO.output(17, GPIO.HIGH)
https://www.raspberrypi.org/learning/physical-computing-with-python/worksheet/

## Slide 10: Raspi GPIO
import RPi.GPIO as GPIO
GPIO.setmode(<mode>)
  GPIO.BOARD
  GPIO.BCM
GPIO.setup(<channel>, <in/out>)
  GPIO.OUT
  GPIO.IN
GPIO.input(<channel>)
GPIO.output(<channel>,<state>)
  GPIO.HIGH
  GPIO.LOW
GPIO.cleanup()
https://www.raspberrypi.org/learning/physical-computing-with-python/
https://sourceforge.net/p/raspberry-gpio-python/wiki/BasicUsage/

## Slide 11: DHT11
Measurement Ranges
  Relative Humidity 20-90%
  Temperature 0-50°C (32-122°F)
Resolution
  1% RH
  1°C (1.8°F)
Accuracy
  ± 5% RH
  ± 2°C (3.6°F)
http://www.micropik.com/PDF/dht11.pdf
https://github.com/szazo/DHT11_Python

## Slide 12: Wiring Diagram – DHT11
https://www.raspberrypi.org/learning/physical-computing-with-python/worksheet/

## Slide 13: PowerSwitch Tail II
Safely switch 120vac appliances
  No dangerous 120vac wiring required
  Isolates Raspberry Pi
  Up to 15 amp
Convenient, easy to use
  Simple as an extension cord
  Two-wire control signal connection
  LED status indicator for debugging
http://www.powerswitchtail.com/Pages/default.aspx
https://cdn-learn.adafruit.com/downloads/pdf/adafruits-raspberry-pi-lesson-13-power-control.pdf

## Slide 14: Wiring Diagram – PST II
https://cdn-learn.adafruit.com/downloads/pdf/adafruits-raspberry-pi-lesson-13-power-control.pdf

## Slide 16: MongoDB
Setup
sudo apt-get mongodb
  **Requires Jessie build of Raspbian
Start Client
mongo
Useful Commands
show dbs
show collections
use <db_name>
db.<db_name>.help()
db.<db_name>.find()

## Slide 17: Flask web microframework
Setup
sudo pip install flask
Why Flask?
Lightweight
Simple to use
Flexible
Extensible
Well documented
https://www.raspberrypi.org/learning/python-web-server-with-flask/

## Slide 18: Getting Started
16 Sensor starter kit, $30 on Amazon
Solderless Breadboard, ~$3-$10
Jumper Wires < $10
Maybe some resistors, < $10
Get deals with kits and a bit of research
PowerSwitch Tail II, $26
http://goo.gl/OjsfSF

## Slide 19: U Can 2!
Chad Boschert
Gravitate Solutions
@chadboschert
www.linkedin.com/in/chadboschert