## Slide 1: IoT and U can 2
Part 2, Controlling the World
Chad Boschert, Gravitate Solutions

## Slide 2: What is the Internet of Things?
  Devices + Network Connectivity + Exchange Data
  Integrating physical world and computer world
  Improved efficiency, accuracy, and economic benefit
https://en.wikipedia.org/wiki/Internet_of_Things
Notes: Network of physical devices - sensing, recording data, sharing data, interacting with each other and their environments
Estimates as high as 50 billion objects by 2020
Easy prototyping with low-cost microcontrollers – Arduino, Pi, and others

## Slide 3: Raspberry Pi
Multiple versions, $5 to ~$40
Raspberry Pi 2
  900MHz quad-cord CPU
  1 GB RAM
  Micro SD card slot
  40 GPIO Pins
  4 USB Ports
  Full HDMI port
  Camera & Display interfaces
  Combined 3.5mm audio jack & composite video
https://www.raspberrypi.org/products/raspberry-pi-2-model-b/
Notes: Reference GPIO pins

## Slide 4: Fermonitor
DIY Wine Fermentation Temperature Control System

## Slide 5: Design Principals
Be lean
  Keep it simple
  Create value
  If it already exists, use it
  Make it work, then improve later if needed
YAGNI
Learn

## Slide 6
Demo Time

## Slide 7: Intro to GPIO
General-Purpose Input/Output
Simply, switches
  Inputs – controlled externally
  Output – controlled by the Pi
Ground
  Zero volts, completes circuits
3.3v
  Provides 3.3 volt power supply
5v
  Provides 5 volt power supply
GPIO #
  Configured as input/output
https://www.raspberrypi.org/learning/physical-computing-with-python/
https://sourceforge.net/p/raspberry-gpio-python/wiki/BasicUsage/

## Slide 8: Simple Circuit
Always On
https://www.raspberrypi.org/learning/physical-computing-with-python/worksheet/

## Slide 9: GPIO Circuit
Programmatically interactive
  switch off/on
GPIO.output(17, GPIO.LOW)
GPIO.output(17, GPIO.HIGH)
https://www.raspberrypi.org/learning/physical-computing-with-python/worksheet/

## Slide 10: DHT11
Measurement Ranges
  Relative Humidity 20-90%
  Temperature 0-50°C (32-122°F)
Resolution
  1% RH
  1°C (1.8°F)
Accuracy
  ± 5% RH
  ± 2°C (3.6°F)
http://www.micropik.com/PDF/dht11.pdf
https://github.com/szazo/DHT11_Python

## Slide 11: Wiring Diagram – DHT11
https://www.raspberrypi.org/learning/physical-computing-with-python/worksheet/

## Slide 12: PowerSwitch Tail II
Safely switch 120vac appliances
  No dangerous 120vac wiring required
  Isolates Raspberry Pi
  Up to 15 amp
Convenient, easy to use
  Simple as an extension cord
  Two-wire control signal connection
  LED status indicator for debugging
http://www.powerswitchtail.com/Pages/default.aspx
https://cdn-learn.adafruit.com/downloads/pdf/adafruits-raspberry-pi-lesson-13-power-control.pdf

## Slide 13: Wiring Diagram – PST II
https://cdn-learn.adafruit.com/downloads/pdf/adafruits-raspberry-pi-lesson-13-power-control.pdf

## Slide 15: Raspi GPIO
import RPi.GPIO as GPIO
GPIO.setmode(<mode>)
  GPIO.BOARD
  GPIO.BCM
GPIO.setup(<channel>, <in/out>)
  GPIO.OUT
  GPIO.IN
GPIO.input(<channel>)
GPIO.output(<channel>,<state>)
  GPIO.HIGH
  GPIO.LOW
GPIO.cleanup()
https://www.raspberrypi.org/learning/physical-computing-with-python/
https://sourceforge.net/p/raspberry-gpio-python/wiki/BasicUsage/

## Slide 16: MongoDB
Setup
sudo apt-get mongodb
  **Requires Jessie build of Raspbian
Start Client
mongo
Useful Commands
show dbs
show collections
use <db_name>
db.<db_name>.help()
db.<db_name>.find()

## Slide 17: Flask web microframework
Setup
sudo pip install flask
Why Flask?
Lightweight
Simple to use
Flexible
Extensible
Well documented
https://www.raspberrypi.org/learning/python-web-server-with-flask/

## Slide 18: Get Started
16 Sensor starter kit, $30 on Amazon
Solderless Breadboard, ~$3-$10
Jumper Wires < $10
Maybe some resistors, < $10
Get deals with kits and a bit of research
PowerSwitch Tail II, $26
http://goo.gl/OjsfSF

## Slide 19: U Can 2!
Chad Boschert
Gravitate Solutions
@chadboschert
www.linkedin.com/in/chadboschert
Notes: Be cautious, but not scared
Use the internet and books