## Slide 1: IoT and U can 2
Part 1, sensing the world
Chad Boschert, Gravitate Solutions

## Slide 2: What is the Internet of Things?
  Devices + Network Connectivity + Exchange Data
  Integrating physical world and computer world
  Improved efficiency, accuracy, and economic benefit
https://en.wikipedia.org/wiki/Internet_of_Things
Notes: The Internet of Things (IoT) is the network of physical objects—devices, vehicles, buildings and other items—embedded withelectronics, software, sensors, and network connectivity that enables these objects to collect and exchange data.[1] The IoT allows objects to be sensed and controlled remotely across existing network infrastructure,[2] creating opportunities for more direct integration of the physical world into computer-based systems, and resulting in improved efficiency, accuracy and economic benefit;[3][4][5][6][7][8] when IoT is augmented with sensors and actuators, the technology becomes an instance of the more general class of cyber-physical systems, which also encompasses technologies such as smart grids, smart homes,intelligent transportation and smart cities. Each thing is uniquely identifiable through its embedded computing system but is able to interoperate within the existing Internet infrastructure. Experts estimate that the IoT will consist of almost 50 billion objects by 2020.[9]

## Slide 3: Excuse me while I… whine about wine

## Slide 4: Fermonitor
DIY Wine Fermentation Temperature Control System

## Slide 5
Demo Time

## Slide 6: Design Principals
Be lean
  Keep it simple
  Create value
  If it already exists, use it
  Make it work, then improve later if needed
YAGNI
Learn

## Slide 7: Raspberry Pi
Multiple versions, $5 to ~$40
Raspberry Pi 2
  900MHz quad-cord CPU
  1 GB RAM
  Micro SD card slot
  40 GPIO Pins
  4 USB Ports
  Full HDMI port
  Camera & Display interfaces
  Combined 3.5mm audio jack & composite video
https://www.raspberrypi.org/products/raspberry-pi-2-model-b/

## Slide 8: DHT11
Measurement Ranges
  Relative Humidity 20-90%
  Temperature 0-50°C (32-122°F)
Resolution
  1% RH
  1°C (1.8°F)
Accuracy
  ± 5% RH
  ± 2°C (3.6°F)
http://www.micropik.com/PDF/dht11.pdf
https://github.com/szazo/DHT11_Python

## Slide 9: Wiring Diagram
https://www.raspberrypi.org/learning/physical-computing-with-python/worksheet/

## Slide 11: Setup your Pi
https://www.raspberrypi.org/downloads/raspbian/
https://www.raspberrypi.org/documentation/configuration/raspi-config.md
  sudo raspi-config
  Expand File System
  Internationalization Options
  Advanced > Hostname
  sudo apt-get update
  sudo apt-get upgraded
  grab coffee or beer…

## Slide 12: MongoDB
Setup
sudo apt-get mongodb
  **Requires Jessie build of Raspbian
Start Client
mongo
Useful Commands
show dbs
show collections
use <db_name>
db.<db_name>.help()
db.<db_name>.find()

## Slide 13: Flask web microframework
Setup
sudo pip install flask
Why Flask?
Lightweight
Simple to use
Flexible
Extensible
Well documented
https://www.raspberrypi.org/learning/python-web-server-with-flask/

## Slide 14: Raspi GPIO
import RPi.GPIO as GPIO
GPIO.setmode(<mode>)
  GPIO.BOARD
  GPIO.BCM
GPIO.setup(<channel>, <in/out>)
  GPIO.OUT
  GPIO.IN
GPIO.input(<channel>)
GPIO.output(<channel>,<state>)
  GPIO.HIGH
  GPIO.LOW
GPIO.cleanup()
https://www.raspberrypi.org/learning/physical-computing-with-python/
https://sourceforge.net/p/raspberry-gpio-python/wiki/BasicUsage/

## Slide 15: U can 2!
16 Sensor starter kit, $30 on Amazon
Solderless Breadboard, ~$3-$10
Jumper Wires < $10
Maybe some resistors, < $10
Get deals with kits and a bit of research
http://goo.gl/OjsfSF